## Slide 1
ACE MATLAB / SimEvents - Session 5 - Methodology
Purpose: replay the same ACE observations through a ground-centric path and a bounded orbital-edge path under the same link rules, then check the SimEvents output
against the stored Excel/MATLAB reference.
1 · SAME INPUT
100 accepted ACE observations
Same arrivals and link schedule
2 · TWO PATHS
Ground: downlink → compute
Edge: compute → reduced downlink
3 · CONTACT WINDOWS
Single server
600 s up / 120 s down
Wait if transmission will not fit
4 · REGRESSION CHECK
Compare every latency
PASS only if max error ≤ 1×10−6
ONE COMMAND
run_simevents
- export ACE inputs
- build Ground / Edge model
- simulate both paths
- compare every result
STORED BASELINE RESULT
(Initial Seed Extracted from Data to test the DES Model, will scale to 10,000 runs)
PASS
200 entity-level comparisons
reported max latency error: 0
Ground mean: 1067.6434 s
Edge mean: 198.2280 s
WHAT PASS MEANS
Model consistency was demonstrated in the stored package.
It hasn’t established measured satellite performance yet.
It does not yet establish H1 as a research finding.
Reproduction is the next gate.